## Slide 1: ROUND ROBIN ARBITER USING UVM TEST BENCH
Mentor TA: ANSHUL
Team #27
SRN | Name
PES1UG23EC098 | DISHA SHETTY
PES1UG22EC125 | HONNASHREE S R
PES1UG23EC192 | NEELAMMA
PES1UG22EC224 | RAAJ S

## Slide 2: DESIGN CODE:
module round_robin_arbiter (
input logic clk,
input logic rst,
input logic [3:0] req,
output logic [3:0] grant
);
typedef enum logic [2:0] {
S_IDLE = 3'b000,
S_0 = 3'b001,
S_1 = 3'b010,
S_2 = 3'b011,
S_3 = 3'b100
} state_t;
state_t present_state, next_state;
// Sequential logic
always_ff @(posedge clk or posedge rst) begin
if (rst)
present_state <= S_IDLE;
else
present_state <= next_state;
end

## Slide 3
// Next-state logic
always_comb begin
next_state = S_IDLE;
unique case (present_state)
S_IDLE: begin
if (req[0]) next_state = S_0;
else if (req[1]) next_state = S_1;
else if (req[2]) next_state = S_2;
else if (req[3]) next_state = S_3;
else next_state = S_IDLE;
end
S_0: begin
if (req[1]) next_state = S_1;
else if (req[2]) next_state = S_2;
else if (req[3]) next_state = S_3;
else if (req[0]) next_state = S_0;
else next_state = S_IDLE;
end
S_1: begin
if (req[2]) next_state = S_2;
else if (req[3]) next_state = S_3;
else if (req[0]) next_state = S_0;
else if (req[1]) next_state = S_1;
else next_state = S_IDLE;
end
S_2: begin
if (req[3]) next_state = S_3;
else if (req[0]) next_state = S_0;
else if (req[1]) next_state = S_1;
else if (req[2]) next_state = S_2;
else next_state = S_IDLE;
end
S_3: begin
if (req[0]) next_state = S_0;
else if (req[1]) next_state = S_1;
else if (req[2]) next_state = S_2;
else if (req[3]) next_state = S_3;
else next_state = S_IDLE;
end
endcase
end
// Output logic
always_comb begin
grant = 4'b0000;
case (present_state)
S_0: grant = 4'b0001;
S_1: grant = 4'b0010;
S_2: grant = 4'b0100;
S_3: grant = 4'b1000;
default: grant = 4'b0000;
endcase
end
endmodule

## Slide 4: LAYERED TESTBENCH:
//==========================================
// UVM Testbench for Round-Robin Arbiter
//==========================================
`include "uvm_macros.svh"
import uvm_pkg::*;
//------------------------------------------
// Transaction
//------------------------------------------
class arb_trans extends uvm_sequence_item;
rand bit [3:0] req;
bit [3:0] gnt;
`uvm_object_utils(arb_trans)
function new(string name = "arb_trans");
super.new(name);
endfunction
function void display(string tag = "");
$display("[%0t] %s req=%b gnt=%b", $time, tag, req, gnt);
endfunction
endclass
//------------------------------------------
// Sequence (Directed + Random)
//------------------------------------------
class arb_seq extends uvm_sequence #(arb_trans);
`uvm_object_utils(arb_seq)
function new(string name = "arb_seq");
super.new(name);
endfunction
virtual task body();
arb_trans tr;
// Phase 1: All 16 request patterns
`uvm_info("SEQ", "Phase 1: All request patterns", UVM_MEDIUM)
for (int i = 0; i < 16; i++) begin
tr = arb_trans::type_id::create("tr");
tr.req = i[3:0];
start_item(tr);
finish_item(tr);
end

## Slide 5
// Phase 2: One-hot patterns
`uvm_info("SEQ", "Phase 2: One-hot patterns", UVM_MEDIUM)
for (int i = 0; i < 4; i++) begin
tr = arb_trans::type_id::create("tr");
tr.req = (1 << i);
start_item(tr);
finish_item(tr);
end
// Phase 3: All high (fairness test)
`uvm_info("SEQ", "Phase 3: Fairness test (all requests)", UVM_MEDIUM)
repeat (12) begin
tr = arb_trans::type_id::create("tr");
tr.req = 4'b1111;
start_item(tr);
finish_item(tr);
end
// Phase 4: Random
`uvm_info("SEQ", "Phase 4: Random patterns", UVM_MEDIUM)
repeat (68) begin
tr = arb_trans::type_id::create("tr");
assert(tr.randomize());
start_item(tr);
finish_item(tr);
end
endtask
endclass

## Slide 6
//------------------------------------------
// Driver
//------------------------------------------
class arb_driver extends uvm_driver #(arb_trans);
`uvm_component_utils(arb_driver)
virtual arb_if vif;
function new(string name = "arb_driver", uvm_component parent = null);
super.new(name, parent);
endfunction
function void build_phase(uvm_phase phase);
if (!uvm_config_db#(virtual arb_if)::get(this, "", "vif", vif))
`uvm_fatal("DRV", "No virtual interface set")
endfunction
virtual task run_phase(uvm_phase phase);
arb_trans tr;
forever begin
seq_item_port.get_next_item(tr);
// Apply request
vif.req = tr.req;
// Wait for clock edge, then capture grant
@(posedge vif.clk);
tr.gnt = vif.gnt;
tr.display("DRIVER");
seq_item_port.item_done();
end
endtask
endclass

## Slide 7
//------------------------------------------
// Monitor + Coverage
//------------------------------------------
class arb_monitor extends uvm_component;
`uvm_component_utils(arb_monitor)
virtual arb_if vif;
// Functional coverage
covergroup arb_cg;
cp_req: coverpoint vif.req {
bins all_patterns[] = {[0:15]};
}
cp_gnt: coverpoint vif.gnt {
bins none = {4'b0000};
bins gnt0 = {4'b0001};
bins gnt1 = {4'b0010};
bins gnt2 = {4'b0100};
bins gnt3 = {4'b1000};
}
endgroup
super.new(name, parent);
arb_cg = new();
endfunction
function void build_phase(uvm_phase phase);
if (!uvm_config_db#(virtual arb_if)::get(this, "", "vif", vif))
`uvm_fatal("MON", "No virtual interface set")
endfunction
task run_phase(uvm_phase phase);
forever begin
@(posedge vif.clk);
if (!vif.rst)
arb_cg.sample();
end
endtask
function void report_phase(uvm_phase phase);
real cov = arb_cg.get_coverage(); $display("\n===================================");
$display(" Functional Coverage = %0.2f%%", cov); $display("===================================\n");
endfunction
endclass
function new(string name = "arb_monitor", uvm_component parent = null);

## Slide 8
//------------------------------------------
// Scoreboard (Checker)
//------------------------------------------
class arb_scoreboard extends uvm_component;
`uvm_component_utils(arb_scoreboard)
function new(string name = "arb_scoreboard", uvm_component parent = null);
super.new(name, parent);
endfunction
// Check grant is one-hot or zero
function bit check_onehot(bit [3:0] gnt);
return (gnt == 4'b0000 || gnt == 4'b0001 ||
gnt == 4'b0010 || gnt == 4'b0100 ||
gnt == 4'b1000);
endfunction
endclass
//------------------------------------------
// Agent
//------------------------------------------
class arb_agent extends uvm_component;
`uvm_component_utils(arb_agent)
uvm_sequencer #(arb_trans) seqr;
arb_driver drv;
arb_monitor mon;
arb_scoreboard scb;
function new(string name = "arb_agent", uvm_component parent = null);
super.new(name, parent);
endfunction
function void build_phase(uvm_phase phase);
seqr = uvm_sequencer#(arb_trans)::type_id::create("seqr", this);
drv = arb_driver::type_id::create("drv", this);
mon = arb_monitor::type_id::create("mon", this);
scb = arb_scoreboard::type_id::create("scb", this);
endfunction
function void connect_phase(uvm_phase phase);
drv.seq_item_port.connect(seqr.seq_item_export);
endfunction
endclass

## Slide 9
//------------------------------------------
// Environment
//------------------------------------------
class arb_env extends uvm_env;
`uvm_component_utils(arb_env)
arb_agent agt;
function new(string name = "arb_env", uvm_component parent = null);
super.new(name, parent);
endfunction
function void build_phase(uvm_phase phase);
agt = arb_agent::type_id::create("agt", this);
endfunction
endclass
//------------------------------------------
// Interface
//------------------------------------------
interface arb_if(input bit clk);
logic rst;
logic [3:0] req;
logic [3:0] gnt;
endinterface

## Slide 10
function void report_phase(uvm_phase phase);
real cov = env.agt.mon.arb_cg.get_coverage();
`uvm_info("COVERAGE", $sformatf("Final Coverage = %.2f%%", cov), UVM_LOW)
if (cov >= 90.0)
`uvm_info("PASS", "*** COVERAGE >= 90%% - TEST PASSED ***", UVM_LOW)
else
`uvm_error("FAIL", $sformatf("Coverage only %.2f%% (goal: 90%%)", cov))
endfunction
endclass
//------------------------------------------
// Test
//------------------------------------------
class arb_test extends uvm_test;
`uvm_component_utils(arb_test)
arb_env env;
arb_seq seq;
function new(string name = "arb_test", uvm_component parent = null);
super.new(name, parent);
endfunction
function void build_phase(uvm_phase phase);
env = arb_env::type_id::create("env", this);
endfunction
task run_phase(uvm_phase phase);
phase.raise_objection(this);
seq = arb_seq::type_id::create("seq");
seq.start(env.agt.seqr);
#100;
phase.drop_objection(this);
endtask

## Slide 11
//------------------------------------------
// Top Module
//------------------------------------------
module tb_top;
bit clk = 0;
always #5 clk = ~clk;
arb_if vif(clk);
round_robin_arbiter dut (
.clk(clk),
.rst(vif.rst),
.req(vif.req),
.gnt(vif.gnt)
);
initial begin
vif.rst = 1;
vif.req = 0;
repeat (3) @(posedge clk);
vif.rst = 0;
end
initial begin
uvm_config_db#(virtual arb_if)::set(null, "*", "vif", vif);
run_test("arb_test");
end
initial begin
$dumpfile("arbiter.vcd");
$dumpvars(0, tb_top);
end
endmodule

## Slide 12
THANK YOU